## Slide 1: NEURON GRID IN SPIKING NEURON NETWORK
Group 03: Nguyen Le Trung – Pham Huy Hoang – Vu Hoang Long

## Slide 2: GENERAL IDEA
NEURON
NETWORK

## Slide 3: TABLE OF CONTENTS
Neuron Structure
Spiking Neuron Network (SNN)
Specifications
  Neuron Grid
  TOP Module
4. Architecture
5. Simulation

## Slide 4: NEURON STRUCTURE
x1
x2
.
.
.
xn
Input
y1
y2
.
.
.
yn
Output

## Slide 5: SPIKING NEURON NETWORK (SNN)[0]
SNN try to mimic the natural behaviors of human’ brain.
Each neuron has a value analogous to the electrical potential of biological neurons at every certain time.
This value can be increased or decreased based on the spikes stream.
If it exceeds some threshold, the neuron will send out an impulse, then the value will instantly drop below its average.
In a SNN, neurons contact with each other by sending and sensing spikes.

## Slide 6
where: is the set of all axons that connect to the current neuron
indicates whether or not there is an incoming spike at j-th axon
is the integrated potential of the current neuron
vi (t) is the potential of neuron i at time t
is the neuron instruction corresponding to j-th axon
is the -th kind of weight of axon j
li is the leak potential of i-th neuron
si indicates whether or not there is an outgoing spike at i-th neuron
is the positive threshold
is the negative threshold
is the positive reset potential
is the negative reset potential
SPECIFICATIONS

## Slide 7: NEURON GRID
Based on RANC[1]
Representation: Matrix: N(a) x N(n)
  N(a) = 256 axons
  N(n) = 256 neurons
Iterate through N(a) axons
Iterate through N(n) neurons
SPECIFICATIONS

## Slide 8: SPECIFICATIONS
NEURON GRID
axon_spikes
256
neuron_parameter
368
neuron_instruction
2
clk
reset_n
tick
neuron_num
8
axon_num
8
scheduler_set
scheduler_clear
spike_out
error
done
update_potential
potential_out
9
256
9
9
9x4
9
9
9
1
9
9
8
4
synapse connections: of considered neuron with 256 axons in core. bit 1 is connected.
current potential: accumulated potential value of neuron
reset potential: the reset value of neuron after releasing a spike
weights 0 to 3: Value of synapse connection’s weight corresponding to considered neuron
leak value: leak potential
positive threshold
negative threshold
reset mode: 2 reset modes of neuron: absoluted and linear
dx value
dy value
axon destination (due to 256 axons)
deliver tick offset
neuron_parameter
TOP MODULE
axon_spikes: spikes information of the entire network
neuron_instruction: refer to the weight types of each axon
scheduler_set: request axon_spikes from the storage
scheduler_clear: clear the information after collected
neuron_num: address where to collect neuron_parameter from RAM
axon_num: address where to collect neuron_instruction from the storage
spike_out: indicate the moment that there is a spike
update_potential: indicate the RAM to update potential_out into neuron_parameter
potential_out: the neuron potential after processed

## Slide 9
SPECIFICATIONS
Waveform

## Slide 10
ARCHITECTURE
Section | Combination of RANC Token Controller and Neuron Block | Neuron Grid
Target Chip Technology | Zynq UltraScale+ MPSoC ZCU106 Evaluation | Zynq UltraScale+ MPSoC ZCU106 Evaluation
Maximum Frequency | 278.86 MHz | 331.90 MHz
Hardware Usage | 235 LUTs, 37 FFs | 277 LUTs, 30 FFs
Detecting Throughput | 676.6 Mbps | 805.3 Mbps
Latency | 66050 clocks | 66048 clocks

## Slide 11
SIMULATION
Verilog simulation
.txt file stores information
C++ simulation
.txt file stores information
compare
C++ Code
generate
.txt file stores

## Slide 12: REFERENCES
[0] "Basic Guide to Spiking Neural Networks for Deep Learning", [Online]. Available: https://cnvrg.io/spiking-neural-networks/
[1] "Spiking neural network", [Online]. Available: https://en.wikipedia.org/wiki/Spiking_neural_network.
[2] Valancius, et al., "FPGA Based Emulation Environment for Neuromorphic Architectures", 2020 IEEE International Parallel and Distributed Processing Symposium Workshops (IPDPSW), New Orleans, LA, USA, pp. 90-97, 2020.
[3] Valancius, et al., "RANC: Reconfigurable Architecture for Neuromorphic Computing", 2020.

## Slide 13: THANK YOU!